Digital Servo MD933

Features:

1. Higher resolution

2. The tightest dead band

3. Accurate positioning

4. Faster control response

5. Quicker acceleration

6. Constant torque throughout the servos travel

7. Increased holding and keeping power when stationary

High resolution—the dead band of most 9g-10g servo with logical chip is 8μs and the resolution is 125.  The resolution of HENGE’s digital servo reaches 3μs, and if used together with HENGE’S high precision dual conversion receiver, the resolution of output signals reaches 1024, which becomes a real high resolution system.

Increased holding power when stationary—many traditional servos with logical chips don’t have a high holding power.

The high holding power of HENGE’s digital servo stems from its high-accuracy MCU, and it has higher PWM frequency compared with the logic chip servo. The digital servo inputs more power to the electromotor to ensure the servo to keep positioning. The servo reflects the control position correctly, even with high torque, it can be in accurate position.  Then, the change of the flight posture caused by environment factors will reduce.

HENGE’S digital servo also possesses higher speed of 0.12sec/60° and higher torque of 2.2kg.cm. It is compatible with FUTABA GY401 gyroscope.  On the electronic helicopter, such as 450 of align, the servo controls the sloping cam plate and tail gyroscope precisely.

HENGE’s digital servo is extremely suitable for the RC which requires high speed, high holding power, high torque and light weight.

Specifications

Control system: +pulse width control 1500uesc neutral

Operating voltage range: 4.8V~6.0V

Operating temperature range: -20℃ to +60℃

Test voltage: 4.8V～6.0v

Operating speed: 0.12/60°

Stall torque: 2.2kg.cm

Idle current: 10mA at stopped

Running current: 200mA/60° no load

Dead band width: ≤3usec

Operating travel: 40°/one side pulse traveling 400usec

Direction: clock wise/pulse traveling 1500 to 1900usec

Motor type: brush DC

Potentiometer type: 2 slider/direct drive

Amplifier type: high efficiency MCU+MOSFET

Dimensions: 22.5x11.5x24.6mm

Weight:12g

Ball bearing: Metal

Gear material: Metal

Connector wire gauge: 28AWG